You can use "CBROM32.EXE" to change P4SCi's LOGO.

Note: The Company logo bitmap file should be

1. 640x480, 256-color format.

2. Change all pictures (company logos) to RGB.

3. Change all pictures (company logos) back to indexed color with Mac OS palette

4. Save all pictures (company logos) file format as windows

Using Adobe Photoshop and change Your Logo to better resolution

- Go to MANU BAR and select "Image" ( Mode ( select RGB color

- Go to MANU BAR and select "Image" ( Mode ( select Indexed color( Palette (   select System (MAC OS) ( OK

- Go to SAVE the Company LOGO

- BMP Options windows will pop up ( select File Format “Windows“( OK.

To change company LOGO:

First, copy the utility (cbrom32) + BIOS file name (e.g. P4SCi.bin) + your logo.bmp (must be 640x480x16bit, bmp file) in one directory then follow the steps below.

Use windows command prompt to make the necessary changes to the file.

- cbrom32 P4SCi.bin /OSB_logo Release (To release company logo from the ROM). Also repeat this step to remove the Intel logo from the screen by using the command “cbrom32 P4SCi.bin /OSB_BMP release. Repeat this step to remove all the OSB BMP (1 to 6).

- cbrom32 P4SCi.bin /OSB_logo “YourLogo”.bmp ( To Add your company logo into the ROM)

- It would combine the picture file "YourLogo.bmp" into the BIOS image "P4SCi.bin".

Then you may verify it with "cbrom32 P4SCi.bin /d" command. You can see the logo file name (CompanyLogo.bmp) and some information in this new ROM image.

- Now use this final P4SCi.bin file to flash the system bios.